## Slide 1
Protocols and Models
Introduction to Networking
CT043-3-1 & Version VE1

## Slide 2: Protocols and Models
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0 (ITN)
Module 3: Protocols and Models

## Slide 4: .
Topic and structure of the Lesson
Topic Title | Topic Objective
The Rules | Describe the types of rules that are necessary to successfully communicate.
Protocols | Explain why protocols are necessary in network communication.
Protocol Suites | Explain the purpose of adhering to a protocol suite.
Standards Organizations | Explain the role of standards organizations in establishing protocols for network interoperability.
Reference Models | Explain how the TCP/IP model and the OSI model are used to facilitate standardization in the communication process.
Data Encapsulation | Explain how data encapsulation allows data to be transported across the network.
Data Access | Explain how local hosts access local resources on a network.
Notes: <number>
3 – Protocols and Models
3.0 – Introduction
3.0.2 – What will I learn to do in this module?

## Slide 6: The Rules
Notes: 3 – Protocols and Models
3.1 – The Rules

## Slide 7: The Rules Communications Fundamentals
Networks can vary in size and complexity. It is not enough to have a connection, devices must agree on “how” to communicate.
There are three elements to any communication:
  There will be a source (sender).
  There will be a destination (receiver).
  There will be a channel (media) that provides for the path of communications to occur.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.2 –Communications Fundamentals

## Slide 8: The Rules Communications Protocols
All communications are governed by protocols.
Protocols are the rules that communications will follow.
These rules will vary depending on the protocol.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.3 – Communications Protocols

## Slide 9: The Rules Rule Establishment
  Individuals must use established rules or agreements to govern the conversation.
  The first message is difficult to read because it is not formatted properly. The second shows the message properly formatted
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.4 – Rules Establishment

## Slide 10: The Rules Rule Establishment (Cont.)
Protocols must account for the following requirements:
  An identified sender and receiver
  Common language and grammar
  Speed and timing of delivery
  Confirmation or acknowledgment requirements
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.4 – Rules Establishment (Cont.)

## Slide 11: The Rules Network Protocol Requirements
Common computer protocols must be in agreement and include the following requirements:
  Message encoding
  Message formatting and encapsulation
  Message size
  Message timing
  Message delivery options
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.5 – Network Protocol Requirements

## Slide 12: The Rules Message Encoding
Encoding is the process of converting information into another acceptable form for transmission.
Decoding reverses this process to interpret the information.
Notes: Messages sent across the network are first converted into bits by the sending host. Each bit is encoded into a pattern of voltages on copper wires, infrared light in optical fibers, or microwaves for wireless systems. The destination host receives and decodes the signals to interpret the message.
3 – Protocols and Models
3.1 – The Rules
3.1.6 – Message Encoding

## Slide 13
Encoding between hosts must be in an appropriate format for the medium.
  Messages sent across the network are converted to bits
  The bits are encoded into a pattern of light, sound, or electrical impulses.
  The destination host must decode the signals to interpret the message.
The Rules Message Encoding
Notes: Messages sent across the network are first converted into bits by the sending host. Each bit is encoded into a pattern of voltages on copper wires, infrared light in optical fibers, or microwaves for wireless systems. The destination host receives and decodes the signals to interpret the message.
3 – Protocols and Models
3.1 – The Rules
3.1.8 – Message Size

## Slide 14: The Rules Message Formatting and Encapsulation
When a message is sent, it must use a specific format or structure.
Message formats depend on the type of message and the channel that is used to deliver the message.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.7 – Message Formatting and Encapsulation

## Slide 15: The Rules Message Size
when a long message is sent from one host to another over a network, it is necessary to break the message into smaller pieces (packets).
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.8 – Message Size

## Slide 16: The Rules Message Timing
Message timing includes the following:
Flow Control – Manages the rate of data transmission and defines how much information can be sent and the speed at which it can be delivered.
Response Timeout – Manages how long a device waits when it does not hear a reply from the destination.
Access method - Determines when someone can send a message.
    There may be various rules governing issues like “collisions”. This is when more than one device sends traffic at the same time and the messages become corrupt.
    Some protocols are proactive and attempt to prevent collisions; other protocols are reactive and establish a recovery method after the collision occurs.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.9 – Message Timing

## Slide 17: The Rules Message Delivery Options
Message delivery may one of the following methods:
  Unicast – one to one communication
  Multicast – one to many, typically not all
  Broadcast – one to all
Note: Broadcasts are used in IPv4 networks, but are not an option for IPv6. Later we will also see “Anycast” as an additional delivery option for IPv6.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.10 – Message Delivery Options

## Slide 18: The Rules A Note About the Node Icon
Documents may use the node icon , typically a circle, to represent all devices.
The figure illustrates the use of the node icon for delivery options.
Notes: 3 – Protocols and Models
3.1 – The Rules
3.1.11 – A Note About the Node Icon
3.1.12 – Check Your Understanding – The Rules

## Slide 19: Protocols
Notes: 3 – Protocols and Models
3.2 – Protocols

## Slide 20: Protocols Network Protocol Overview
Network protocols define a common set of rules.
Can be implemented on devices in:
  Software
  Hardware
  Both
Protocols have their own:
  Function
  Format
  Rules
Protocol Type | Description
Network Communications | enable two or more devices to communicate over one or more networks
Network Security | secure data to provide authentication, data integrity, and data encryption
Routing | enable routers to exchange route information, compare path information, and select best path
Service Discovery | used for the automatic detection of devices or services
Notes: 3 – Protocols and Models
3.2 – Protocols
3.2.1 – Network Protocol Overview

## Slide 21: Protocols Network Protocol Functions
Devices use agreed-upon protocols to communicate .
Protocols may have one or more functions.
Function | Description
Addressing | Identifies sender and receiver
Reliability | Provides guaranteed delivery
Flow Control | Ensures data flows at an efficient rate
Sequencing | Uniquely labels each transmitted segment of data
Error Detection | Determines if data became corrupted during transmission
Application Interface | Process-to-process communications between network applications
Notes: 3 – Protocols and Models
3.2 – Protocols
3.2.2 – Network Protocol Functions

## Slide 22: Protocols Protocol Interaction
When we use network, we require the use of several protocols.
Each protocol has its own function and format.
Protocol | Function
Hypertext Transfer Protocol (HTTP) | Governs the way a web server and a web client interact Defines content and format
Transmission Control Protocol (TCP) | Manages the individual conversations Provides guaranteed delivery Manages flow control
Internet Protocol (IP) | Delivers messages globally from the sender to the receiver
Ethernet | Delivers messages from one NIC to another NIC on the same Ethernet Local Area Network (LAN)
Notes: 3 – Protocols and Models
3.2 – Protocols
3.2.3 – Protocol Interaction
3.2.4 – Check Your Understanding - Protocols

## Slide 23: Protocol Suites
Notes: 3 – Protocols and Models
3.3 – Protocol Suites

## Slide 24: Protocol Suites Network Protocol Suites
Protocols must be able to work with other protocols.
Protocol suite:
  A group of inter-related protocols necessary to perform a communication function
  Sets of rules that work together to help solve a problem
The protocols are viewed in terms of layers:
  Higher Layers
  Lower Layers- concerned with moving data and provide services to upper layers
Notes: 3 – Protocols and Models
3.3 – Protocol Suites
3.3.1 – Network Protocol Suites

## Slide 25: Protocol Suites Evolution of Protocol Suites
There are several protocol suites.
Internet Protocol Suite or TCP/IP- The most common protocol suite and maintained by the Internet Engineering Task Force (IETF)
Open Systems Interconnection (OSI) protocols- Developed by the International Organization for Standardization (ISO) and the International Telecommunications Union (ITU)
AppleTalk- Proprietary suite release by Apple Inc.
Novell NetWare- Proprietary suite developed by Novell Inc.
Notes: Rules in driving, now all set together under one booklet, we can think of that as the protocol suite
3 – Protocols and Models
3.3 – Protocol Suites
3.3.2 – Evolution of Protocol Suites

## Slide 26: Protocol Suites TCP/IP Protocol Example
TCP/IP protocols operate at the application, transport, and internet layers.
The most common network access layer LAN protocols are Ethernet and WLAN (wireless LAN).
Notes: 3 – Protocols and Models
3.3 – Protocol Suites
3.3.3 – TCP/IP Protocol Example

## Slide 27: Protocol Suites TCP/IP Protocol Suite
TCP/IP is the protocol suite used by the internet and includes many protocols.
TCP/IP is:
  An open standard protocol suite that is freely available to the public and can be used by any vendor
  A standards-based protocol suite that is endorsed by the networking industry and approved by a standards organization to ensure interoperability
Notes: 3 – Protocols and Models
3.3 – Protocol Suites
3.3.4 – TCP/IP Protocol Suite

## Slide 28: Protocol Suites TCP/IP Communication Process
A web server encapsulating and sending a web page to a client.
A client de-encapsulating the web page for the web browser
Notes: Each layer is related to each other as they take upper level data and add extra information: encapsulation
3 – Protocols and Models
3.3 – Protocol Suites
3.3.5 – TCP/IP Communication Process
3.3.6 – Check Your Understanding – Protocol Suites

## Slide 29: Standards Organizations
Notes: 3 – Protocols and Models
3.4 – Standards Organizations

## Slide 30: Standards Organizations Open Standards
Open standards encourage:
interoperability
competition
innovation
Standards organizations are:
vendor-neutral
non-profit organizations
established to develop and promote the concept of open standards.
Notes: 3 – Protocols and Models
3.4 – Standards Organizations
3.4.1 – Open Standards

## Slide 31: Standards Organizations Internet Standards
Internet Society (ISOC) - Promotes the open development and evolution of internet
Internet Architecture Board (IAB) - Responsible for management and development of internet standards
Internet Engineering Task Force (IETF) - Develops, updates, and maintains internet and TCP/IP technologies
Internet Research Task Force (IRTF) - Focused on long-term research related to internet and TCP/IP protocols
Notes: 3 – Protocols and Models
3.4 – Standards Organizations
3.4.2 – Internet Standards

## Slide 32: Standards Organizations Internet Standards (Cont.)
Standards organizations involved with the development and support of TCP/IP
  Internet Corporation for Assigned Names and Numbers (ICANN) - Coordinates IP address allocation, the management of domain names, and assignment of other information
  Internet Assigned Numbers Authority (IANA) - Oversees and manages IP address allocation, domain name management, and protocol identifiers for ICANN
Notes: 3 – Protocols and Models
3.4 – Standards Organizations
3.4.2 – Internet Standards (Cont.)

## Slide 33: Standards Organizations Electronic and Communications Standards
Institute of Electrical and Electronics Engineers (IEEE, pronounced “I-triple-E”) - dedicated to creating standards in power and energy, healthcare, telecommunications, and networking
Electronic Industries Alliance (EIA) - develops standards relating to electrical wiring, connectors, and the 19-inch racks used to mount networking equipment
Telecommunications Industry Association (TIA) - develops communication standards in radio equipment, cellular towers, Voice over IP (VoIP) devices, satellite communications, and more
International Telecommunications Union-Telecommunication Standardization Sector (ITU-T) - defines standards for video compression, Internet Protocol Television (IPTV), and broadband communications, such as a digital subscriber line (DSL)
Notes: 3 – Protocols and Models
3.4 – Standards Organizations
3.4.3 – Electronic and Communications Standards

## Slide 34: Reference Models
Notes: 3 – Protocols and Models
3.5 – Reference Models

## Slide 35: Reference Models The Benefits of Using a Layered Model
Complex concepts such as how a network operates can be difficult to explain and understand. For this reason, a layered model is used.
Two layered models describe network operations:
Open System Interconnection (OSI) Reference Model
TCP/IP Reference Model
Notes: 3 – Protocols and Models
3.5 – Reference Models
3.5.1 – The Benefits of Using a Layered Model

## Slide 36: Reference Models The Benefits of Using a Layered Model (Cont.)
These are the benefits of using a layered model:
Assist in protocol design because protocols that operate at a specific layer have defined information that they act upon and a defined interface to the layers above and below
Foster competition because products from different vendors can work together
Prevent technology or capability changes in one layer from affecting other layers above and below
Provide a common language to describe networking functions and capabilities
Notes: 3 – Protocols and Models
3.5 – Reference Models
3.5.1 – The Benefits of Using a Layered Model (Cont.)

## Slide 37: Reference Models The OSI Reference Model
OSI Model Layer | Description
7 - Application | Contains protocols used for process-to-process communications.
6 - Presentation | Provides for common representation of the data transferred between application layer services.
5 - Session | Provides services to the presentation layer and to manage data exchange.
4 - Transport | Defines services to segment, transfer, and reassemble the data for individual communications.
3 - Network | Provides services to exchange the individual pieces of data over the network.
2 - Data Link | Describes methods for exchanging data frames over a common media.
1 - Physical | Describes the means to activate, maintain, and de-activate physical connections.
Notes: 3 – Protocols and Models
3.5 – Reference Models
3.5.2 – The OSI Reference Model

## Slide 38: Reference Models The TCP/IP Reference Model
TCP/IP Model Layer | Description
Application | Represents data to the user, plus encoding and dialog control.
Transport | Supports communication between various devices across diverse networks.
Internet | Determines the best path through the network.
Network Access | Controls the hardware devices and media that make up the network.
Notes: 3 – Protocols and Models
3.5 – Reference Models
3.5.3 – The TCP/IP Reference Model

## Slide 39: Reference Models OSI and TCP/IP Model Comparison
The OSI model divides the network access layer and the application layer of the TCP/IP model into multiple layers.
The TCP/IP protocol suite does not specify which protocols to use when transmitting over a physical medium.
OSI Layers 1 and 2 discuss the necessary procedures to access the media and the physical means to send data over a network.
Notes: 3 – Protocols and Models
3.5 – Reference Models
3.5.4 – OSI and TCP/IP Model Comparison

## Slide 40: Data Encapsulation
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation

## Slide 41: Data Encapsulation Segmenting Messages
Segmenting is the process of breaking up messages into smaller units.
Multiplexing is the processes of taking multiple streams of segmented data and interleaving them together.
Segmenting messages has two primary benefits:
Increases speed - Large amounts of data can be sent over the network without tying up a communications link.
Increases efficiency - Only segments which fail to reach the destination need to be retransmitted, not the entire data stream.
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation
3.6.1 – Segmenting Messages

## Slide 42: Data Encapsulation Sequencing
Sequencing messages is the process of numbering the segments so that the message may be reassembled at the destination.
TCP is responsible for sequencing the individual segments.
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation
3.6.2 – Sequencing

## Slide 43: Data Encapsulation Protocol Data Units (PDU)
Encapsulation is the process where protocols add their information to the data.
At each stage of the process, a PDU has a different name to reflect its new functions.
There is no universal naming convention for PDUs, in this course, the PDUs are named according to the protocols of the TCP/IP suite.
PDUs passing down the stack are as follows:
  Data (Data Stream)
  Segment
  Packet
  Frame
  Bits (Bit Stream)
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation
3.6.3 – Protocol Data Units

## Slide 44: Data Encapsulation Encapsulation Example
Encapsulation is a top down process.
The level above does its process and then passes it down to the next level of the model. This process is repeated by each layer until it is sent out as a bit stream.
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation
3.6.4 – Encapsulation Example

## Slide 45: Data Encapsulation De-encapsulation Example
Data is de-encapsulated as it moves up the stack.
When a layer completes its process, that layer strips off its header and passes it up to the next level to be processed. This is repeated at each layer until it is a data stream that the application can process.
  Received as Bits (Bit Stream)
  Frame
  Packet
  Segment
  Data (Data Stream)
Notes: 3 – Protocols and Models
3.6 – Data Encapsulation
3.6.5 – De-encapsulation Example
3.6.6 – Check Your Understanding – Data Encapsulation

## Slide 46: Data Access
Notes: 3 – Protocols and Models
3.7 – Data Access

## Slide 47: Data Access Addresses
Both the data link and network layers use addressing to deliver data from source to destination.
Network layer source and destination addresses - Responsible for delivering the IP packet from original source to the final destination.
Data link layer source and destination addresses – Responsible for delivering the data link frame from one network interface card (NIC) to another NIC on the same network.
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.1 – Addresses

## Slide 48: Data Access Layer 3 Logical Address
The IP packet contains two IP addresses:
  Source IP address - The IP address of the sending device, original source of the packet.
  Destination IP address - The IP address of the receiving device, final destination of the packet.
These addresses may be on the same link or remote.
Notes: IP : Home address (Global)
3 – Protocols and Models
3.7 – Data Access
3.7.2 – Layer 3 Logical Address

## Slide 49: Data Access Layer 3 Logical Address (Cont.)
An IP address contains two parts:
Network portion (IPv4) or Prefix (IPv6)
  The left-most part of the address indicates the network group which the IP address is a member.
  Each LAN or WAN will have the same network portion.
Host portion (IPv4) or Interface ID (IPv6)
  The remaining part of the address identifies a specific device within the group.
  This portion is unique for each device on the network.
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.2 – Layer 3 Logical Address (Cont.)

## Slide 50: Data Access Devices on the Same Network
When devices are on the same network the source and destination will have the same number in network portion of the address.
  PC1 – 192.168.1.110
  FTP Server – 192.168.1.9
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.3 – Devices on the Same Network-

## Slide 51: Data Access Role of the Data Link Layer Addresses: Same IP Network
When devices are on the same Ethernet network the data link frame will use the actual MAC address of the destination NIC.
MAC addresses are physically embedded into the Ethernet NIC and are local addressing.
The Source MAC address will be that of the originator on the link.
The Destination MAC address will always be on the same link as the source, even if the ultimate destination is remote.
Notes: IP : Home address (Global) MAC: Person Name (At Home)
3 – Protocols and Models
3.7 – Data Access
3.7.4 – Role of the Data Link Layer Addresses: Same IP Network

## Slide 52: Data Access Devices on a Remote Network
What happens when the actual (ultimate) destination is not on the same LAN and is remote?
What happens when PC1 tries to reach the Web Server?
Does this impact the network and data link layers?
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.5 – Devices on a Remote Network

## Slide 53: Data Access Role of the Network Layer Addresses
When the source and destination have a different network portion, this means they are on different networks.
  PC1 – 192.168.1
  Web Server – 172.16.1
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.6 – Role of the Network Layer Addresses

## Slide 54: Data Access Role of the Data Link Layer Addresses: Different IP Networks
When the final destination is remote, Layer 3 will provide Layer 2 with the local default gateway IP address, also known as the router address.
The default gateway (DGW) is the router interface IP address that is part of this LAN and will be the “door” or “gateway” to all other remote locations.
All devices on the LAN must be told about this address or their traffic will be confined to the LAN only.
Once Layer 2 on PC1 forwards to the default gateway (Router), the router then can start the routing process of getting the information to actual destination.
Notes: When Packet is to different network, the IP address will always remain the same
But the MAC address source and destination changes from one hop to another hop (Parcel from Japan to Malaysia, hub by hub)
3 – Protocols and Models
3.7 – Data Access
3.7.7 – Role of the Data Link Layer Addresses: Different IP Networks

## Slide 55: Data Access Role of the Data Link Layer Addresses: Different IP Networks (Cont.)
The data link addressing is local addressing so it will have a source and destination for each link.
The MAC addressing for the first segment is :
  Source – AA-AA-AA-AA-AA-AA (PC1) Sends the frame.
  Destination – 11-11-11-11-11-11 (R1- Default Gateway MAC) Receives the frame.
Note: While the L2 local addressing will change from link to link or hop to hop, the L3 addressing remains the same.
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.7 – Role of the Data Link Layer Addresses: Different IP Networks (Cont.)

## Slide 56: Data Access Data Link Addresses
Since data link addressing is local addressing, it will have a source and destination for each segment or hop of the journey to the destination.
The MAC addressing for the first segment is:
  Source – (PC1 NIC) sends frame
  Destination – (First Router- DGW interface) receives frame
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.8 – Data Link Addresses

## Slide 57: Data Access Data Link Addresses (Cont.)
The MAC addressing for the second hop is:
  Source – (First Router- exit interface) sends frame
  Destination – (Second Router) receives frame
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.8 – Data Link Addresses (Cont.)

## Slide 58: Data Access Data Link Addresses (Cont.)
The MAC addressing for the last segment is:
  Source – (Second Router- exit interface) sends frame
  Destination – (Web Server NIC) receives frame
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.8 – Data Link Addresses (Cont.)

## Slide 59: Data Access Data Link Addresses (Cont.)
Notice that the packet is not modified, but the frame is changed, therefore the L3 IP addressing does not change from segment to segment like the L2 MAC addressing.
The L3 addressing remains the same since it is global and the ultimate destination is still the Web Server.
Notes: 3 – Protocols and Models
3.7 – Data Access
3.7.8 – Data Link Addresses (Cont.)

## Slide 60: .
https://www.youtube.com/watch?v=xaKvGnnuYmk

## Slide 61: Summary
Notes: 4-Physical Layer
4.8 - Summary

## Slide 62: Summary / Recap of Main Points

## Slide 63: Q & A

## Slide 64: What To Expect Next Week
In Class
Application Layer